## Slide 1
This is v4.0 of the homemade, non-powered automatic water level controller controls the high and low water(or nutrient) level of the hydroponic system.
By Billy Cheung 2019-Nov-23
Youtube: BillyDiyDreamShop
Blog: https://billydiy.blogspot.hk
https://github.com/cheungbx
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 2
Big
Nutrient Tank
Homemade Auto pot v4.0

## Slide 3
High water level control avoids flooding.
Low water level control only replenishes water when it drops below a low level set by the notches (brown).
Create ample space for roots to breath which is essential for a healthy growth.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 4
Advantages over DWC (Deep Water Culture):
Creates ample space for the roots to breath for healthier growth
Better PH control as a smaller amount of nutrient is stored inside the growth bed and replenished continuously.
Run automatically over a longer period
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 5
Nutrient solution is supplied by a big tank to the unit through the inlet nozzle (yellow) .
The air pipe (orange) is sealed by the outer float valve (green)
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 6
3. When the solution level rises , the inner float valve (purple) is lifted a bit.
4. When the level goes beyond the low level defined by the notches at the bottom (brown), the space inside the unit is sealed and the inner float valve cannot be lifted further due to air pressure.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 7
5. When the solution level rises further , the outer float valve (green) is lifted opening up the air pipe (orange).
6. This allows the inner float valve to lift up to the top to seal the inlet (yellow) stopping solutions inflow.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 8
7. The plant consumes the nutrient solution causing the level to drop.
8. The outer float valve (green) will fall and seal the air pipe (orange) creating a vacuum inside the unit.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 9
10. The level continues to drop, but the vacuum condition keeps the solution inside the controller unit supporting the float valve that continues to block the nozzle (yellow ) and continue to stop the inflow.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 10
11. When the level drops below the low level mark which is set by the notches at the base of the Unit, the vacuum is broken and the solution inside the unit is released lowering the float valve.
12. The water inlet will be unblocked allowing the growth bed to be refilled with the nutrient solution again.
Big Nutrient Tank
Homemade Auto pot v4.0

## Slide 11
13. The cycle repeats until all nutrient solution in the bigger nutrient tank runs out.
Big Nutrient Tank
Homemade Auto pot v4.0